## Slide 1
Symbiosis Skills and Professional University
Village – Kiwale, Adjoining Pune Mumbai Expressway, Pune – 412101,
Maharashtra, India.
A
Presentation on
Design and Fabrication of Mecanum Wheels for Forklift Applications
Under the Guidance of:
Mr. Rajkumar Baghel

## Slide 2: Team Members
Karan S. Tomar (1900501018)
Kishan Gohel (1900501022)
Krutarth Gohel (1900501023)
Jay Hiran (1900501029)
Navodit Sankhyan (1800501019)
SCHOOL OF AUTOMOBILE ENGINEERING

## Slide 3: Contents
Mecanum Wheel Introduction
Objectives
Methodology
Literature Survey
Components
Construction
SCHOOL OF AUTOMOBILE ENGINEERING

## Slide 4: Contents
CAD Models
Plan Of Execution
Applications
Advantages
Future Scope
Conclusion
SCHOOL OF AUTOMOBILE ENGINEERING

## Slide 5
Problem Statement
SCHOOL OF AUTOMOBILE ENGINEERING
A wheel system that can provide omnidirectional movement for the forklifts.
A wheel system allowing forklift to move in any direction without changing its orientation.
This could be particularly useful in tight spaces where maneuverability is limited, such as in warehouses or factories.
Increasing efficiency of material movement by reducing travelling distance.

## Slide 6: Mecanum Wheel Introduction
It is an omnidirectional wheel for vehicle to maneuver in any direction.
It is a form of tireless wheel.
It has series of rubberized external rollers.
The rollers are obliquely attached to the rim.
The rollers have an axis of rotation at 45° to the wheel plane.
The rollers have an axis of rotation at 45° to the axle line.
SCHOOL OF AUTOMOBILE ENGINEERING

## Slide 7: Mecanum Wheel in Forklift
SCHOOL OF AUTOMOBILE ENGINEERING

## Slide 8
Literature Survey
These are similar to tracked chain vehicle system.
These provides better maneuverability.
It has series of rubberized external rollers.
Rollers are obliquely attached to rim.
Rollers have axis of rotation at 45° to wheel plane.
Rollers have axis of rotation at 45° to axle line.
SCHOOL OF AUTOMOBILE ENGINEERING

## Slide 9
Literature Survey
Each wheel is non-steering drive wheel.
Each wheel is independent and has its own powertrain.
Wheel spinning generates propelling force.
This force is perpendicular to roller axle.
It is then vectored into a longitudinal component.
And also transverse component.
SCHOOL OF AUTOMOBILE ENGINEERING

## Slide 10: Project Flowchart
SCHOOL OF AUTOMOBILE ENGINEERING
Literature Survey
Define Objective
Material Selection
Fabrication
Conclusion
Design Of Physical Model
Understand Problem Statement

## Slide 11
Plan Of Execution
SCHOOL OF AUTOMOBILE ENGINEERING

## Slide 12
To be able to design Mecanum wheel.
To able use the wheel to help the vehicle maneuver in different directions.
To able use the wheel to help the vehicle maneuver in different directions.
To develop a low cost prototype model of Mecanum Wheel.
Objectives
SCHOOL OF AUTOMOBILE ENGINEERING

## Slide 13
Methodology
SCHOOL OF AUTOMOBILE ENGINEERING

## Slide 14
Direction of movement | Wheel actuation
Forward | All wheels forward same speed
Reverse | All wheels backward same speed
Right shift | Wheel 1-4 forward Wheel 2-3 backward
Left shift | Wheel 2-3 forward Wheel 1-4 backward
Clockwise turn | Wheel 1-3 forward Wheel 2-4 backward
Counter clockwise turn | Wheel 2-4 forward Wheel 1-3 backward
Methodology
SCHOOL OF AUTOMOBILE ENGINEERING

## Slide 15
Working Animation
SCHOOL OF AUTOMOBILE ENGINEERING

## Slide 16
Components
SCHOOL OF AUTOMOBILE ENGINEERING
Frame
Rubberized Roller
Arduino Uno
Motor
Power Supply (Power Bank)
Chassis
Circuit (Power Distribution)

## Slide 17
CAD Models and Drawings
SCHOOL OF AUTOMOBILE ENGINEERING

## Slide 18
CAD Models and Drawings
SCHOOL OF AUTOMOBILE ENGINEERING

## Slide 19
Can help the vehicle move in any direction.
There is no additional friction while turning.
It allows for in-place rotation with minimal ground friction.
It also allows for in-place rotation with low torque.
It is much simpler and more reliable than crab drive system.
Advantages
SCHOOL OF AUTOMOBILE ENGINEERING

## Slide 20
Mecanum Wheels are marginally heavier than their conventional counterparts.
They cost higher.
The smaller contact area disables its use in passenger cars.
Used for low speed drive.
Vertical and horizontal vibrations.
Future Scope
SCHOOL OF AUTOMOBILE ENGINEERING

## Slide 21
Wheel chairs
Automated Guided Vehicles (AGV)
Military vehicles
Forklift trucks
Flexible Parking
Shopping cart
Applications
SCHOOL OF AUTOMOBILE ENGINEERING

## Slide 22
Conclusion
SCHOOL OF AUTOMOBILE ENGINEERING
The Mecanum wheel is a design for a wheel which can move a vehicle in any direction and can perform in-place rotation.
Tracked vehicles and skid steer vehicles utilize similar methods for turning. However, these vehicles typically drag across the ground while turning and may do considerable damage to a soft or fragile surface.
Compared to skid steer, Mecanum wheels have no additional friction when turning which is an advantage.

## Slide 23
Conclusion
SCHOOL OF AUTOMOBILE ENGINEERING
By comparison, the design of the Mecanum wheel allows for in-place rotation with minimal ground friction and low torque.
Mecanum wheels will be simpler and perhaps more reliable than a swerve/crab drive system.
It cannot be used in regular car because it is usually used for low-speed drive.

## Slide 24
Prototype
SCHOOL OF AUTOMOBILE ENGINEERING

## Slide 25
Thank
You
SCHOOL OF AUTOMOBILE ENGINEERING